## Slide 1: Summer Internship
Zara Weir

## Slide 2: Physics Informed Machine Learning
Taking small data and more physics to build models
Can include the physics as observational bias (like data from sensors), inductive bias (like applying PDEs in the loss function in a PINN), and learning bias (like including penalties)
Good for noisy data, or small amounts of data, and for high-dimensional problems
There’s different uncertainties due to the physics, the data, and the model
Can be used in many applications

## Slide 3: Rolling Bearing
Simulation of a non-linear model of the rolling bearing
Looks at amplitude as a function of clearance
There’s a mix of period and chaotic vibrations
Small change in clearance can result in a large change in the amplitude

## Slide 4: SINDy
Sparse Identification of Nonlinear Dynamics
Dynamic system
We take time series data to find system models

## Slide 6: Implicit-SINDy
If we need to find implicit differential equations
Now, the problem looks like this
But this doesn’t work well with noise

## Slide 7: SINDy-PI
From implicit-SINDy, assuming we know 1 term from the library that’s in the dynamics, the problem is rewritten non-implicit
We minimise the loss function

## Slide 9: SINDy examples in MATLAB
Lorenz system example
Actual
Approximated
Xi matrix

## Slide 10: Graph Representation

## Slide 11: SINDy-PI examples in MATLAB
Double pendulum example

## Slide 12: ODEs

## Slide 13: Graph representation
Time plot
Phase plot

## Slide 14: Lotka-Volterra Equations in SINDy
The equations used
From SINdy

## Slide 15: Time plot
Expected solutions
From SINDy

## Slide 16: Phase plot
Expected solutions
From SINDy

## Slide 17: Lotka-Volterra Equations in SINDy-PI
Based on the constrained formulation example
  Testing all candidate models at once
This was taking too long to run in MATLAB so moved on to Python

## Slide 18: PySINDy – Python SINDy package
Has different implementations of SINDy, written in python
Reproduced Lorenz system example
Notes: Took some trial and error and getting refamiliarised with spyder. See PySINDy tests doc for more detail

## Slide 19: Abrupt-SINDy
Used to detect abrupt changes in the system
  Baseline model from SINDy detects abrupt change  updates model

## Slide 20: SINDy with control
Using Model predictive control (MPC)
  Need to look more at

## Slide 21: SINDy-SA (Sensitivity Analysis)
Determines the hyperparameters

## Slide 22: Ensemble-SINDy

## Slide 23: Further roller bearing papers
SCNN for fault detection (in roller bearing)
  CNN based approach, with signal preprocessing
Nonlinear model and simulation of a rolling bearing
  Equations found:
Effect of the raceway defects on the nonlinear dynamic behavior of rolling
Notes: See literature review doc for further comments

## Slide 24: Lotka-Volterra in pysindy – SINDy
Initially based of Lorenz example – didn’t work
Then based off of 2D Linear ODE example
  Just solves equations given (so should be exact)
(x0)' = 0.050 x0 + -0.005 x0 x1
(x1)' = -0.200 x1 + 0.005 x0 x1
Notes: Lots of trial and error with this stage
Initially copied from the Lorenz system example as this is what I’d done w/ the matlab, but it wasn’t working right, then tried to copy from the basic example (in the readme) but realised this needs you to put in the solutions to your ODEs. Then tried it with the example ‘2D linear ODEs from example 3 original paper, and after toggling with lambda (sparsity parameter) and time, got what was expected.
Also as part of this process tried to run examples for the SINDy-SA github, but having issues with modules
See PySINDy tests doc for more detail

## Slide 25: SINDy-PI in pysindy
Replicated example using SINDy-PI method
Bacterial system
x0_dot = -0.426 x0 + 0.008 x1 + -0.001 x1x1x1x1
x1_dot = 0.239 x1 + -0.336 x1x1 + 0.090 x1x1x1x1 + -0.020 x1x1x1x1x1 + 0.001 x1x1x1x1x1x1 + 0.975 x0x1_dot + 1.089 x1x1_dot + -0.024 x1x1x1x1_dot + -0.014 x1x1x1x1x1x1x1_dot

## Slide 26: Rolling bearing equations in pysindy
Since the rolling bearing equations are 2nd order ODEs, the SINDy-PI method has to be used
Have to rewrite the equations as a system of 1st order ODEs
Before looking at applying SINDy, will identify a ground truth – i.e. solve the equations found in the literature

## Slide 27: Simplified Rolling Bearing Equations
Simplified equations – making terms linear, breaking down the equations
  Based on equations given in Simulation and Analysis of Vibration of Rolling Bearing
Replaced the terms with constants
The damping force term
Notes: Solution, when all the terms are linear was a straight line as expected
Don’t think the damping force one is correct – come back to

## Slide 28: Changing the forcing term in F = ma ()
Spring, damper, trig terms
Plotting the displacement, velocity, and acceleration
Spring force
Damping force
Sinusoidal force
Notes: Made the equations even simpler – start from 2nd law
Plotted displacement, velocity and acceleration for constant F, spring, damper, sinusoidal, and combinations of these

## Slide 29: Combining forcing terms

## Slide 30: AIC and BIC
Model selection methods
If SINDy has multiple iterations producing multiple models, this helps us choose the best one
AIC considers how strongly the model fits the data and the number of parameters
BIC also considers the number of samples
Notes: Akaike and Bayesian Information Criterion
Where k is no of parameters, L is the log-likelihood, and n is the number of samples

## Slide 31: Synthetic data
Using the spring damper and sin term system to generate ‘synthetic data’ for testing variations of SINDy
SINDy, Abrupt-SINDy, SINDy-PI, Ensemble SINDy

## Slide 32: Noisy Data
Added noise to the ‘synthetic data’ to see if dynamics could be recovered by SINDy
SINDy (original)
(x0)' = 0.989 x1
(x1)' = 1.693 1 + 1.693 1 + -0.672 x0 + -0.118 x1 + -1.036 x1^2
Ensemble with replacement (V1)
(x0)' = 0.095 1 + 0.095 1 + -0.037 x0 + 0.952 x1 + -0.023 x1^2
(x1)' = 1.693 1 + 1.693 1 + -0.672 x0 + -0.118 x1 + -1.036 x1^2
Combination Ensemble (V4)
(x0)' = 0.989 x1
(x1)' = 1.693 1 + 1.693 1 + -0.672 x0 + -0.118 x1 + -1.036 x1^2

## Slide 33: Case Western data
Accelerometer data from ball bearing tests for normal operation and faults under different operation conditions
Histogram
Time Series

## Slide 34: Case Western data in SINDy
SINDy Model
(x0)' = 0.004 x0 + -0.064 x0^2 + -0.132 x0^3 + 0.518 x0^4
x0_t = -0.0002 1 + -0.0009 sin(t) + -0.0002 1 + -0.0006 x0 + 0.0114 x0^2 + -0.0025 x0^3 + -0.0159 x0^4 + 0.0063 x0^5 + 0.0009 x0^6

## Slide 35: Other papers on (PI)ML
Science Autonomy and Space Science: Application to the ExoMars Mission
Incorporating Physical Knowledge into Machine Learning for Planetary Space Physics

## Slide 36: NASA Bearing dataset
(x0)' = -0.007 1 + 0.494 x0 + -10.244 x0^2 + 83.012 x0^3 + -265.069 x0^4 + 281.022 x0^5
(x0)' = -0.007 1 + 0.494 x0 + -10.244 x0^2 + 83.012 x0^3 + -265.069 x0^4 + 281.022 x0^5
Ensemble-SINDy
x0 = 0.0138 1 + 0.0200 x0_t + 0.0048 x0_tt + 0.0138 1 + 0.0002 x0 + 12.5113 x0^2 + -64.1203 x0^3 + 114.2033 x0^4 + 3.3844 x0^5 + -38.6638 x0^6
SINDy-PI

## Slide 37: Final Findings
The best result on real data is using SINDy-PI to recover dynamics from the NASA Bearing dataset